### 5 MONITORS MIXES

M1	VOC 1, 2 & 3, GUITAR 2, KICK, HI-HAT, SNARE, BASS, CONGAS

M2	VOC 1, 2, 3 & 4, TRUMPET, TROMBONE & SAX, GUITAR 2, HI-HAT

M3	VOC 1, 2, 3 & 4, GUITAR 1, HI-HAT, KICK, CONGAS

M4       KICK, GUITAR 2, BASS, CONGAS, HORNS

M5	CONGAS (!), KICK, SNARE, HI-HAT, RACK & FLOOR TOMS, BASS

### BACKLINE REQUIRED

1 Drum Set Mapex saturn series (our drummer is official Mapex artist) or analog export with kick 20” + 10” & 12” rack toms + 14” floor tom + 6 stands for cymbals and hi-hat + all hardware and stool .

2 Congas 11” & 11.3/4” type LP Professional series or analog and stool.

Timbales14"&15" type LP Professional series or analog.

Gtr amp1: Fender Twin Reverb , Mesa Boogie , Fender Blues Deluxe , min 100 watt

Gtr amp2: Fender Twin Reverb , Fender Tone-master , Mesa Boogie , min 100 watt

No any Marshall , please, if it possible.

Bass amp: Ampeq SVT , Hartke ,Trace Eliott min. 300 watt

P.A. SYSTEM:

P.A. System must be about 15-20 watt per each person in a house.

EAW , MARTIN AUDIO , EV preferred.

Channel Instrument Mic / Type Insert Special 1 Kick Drum Akg D112 /Shure B52 Gate 2 Snare 1 Top Shure sm57/Beta57 Compr Gate 3 Snare 1 Btm Shure sm98/sm57 Compr Gate 4 Hi Hat Akg 451/460 5 Rack tom 1 Shure sm98/md 421 Gate 6 Rack tom 2 Shure sm98/md 421 Gate 7 Floor tom Shure sm98/md 421 Gate 8 Overhead L Akg 451/460 9 Overhead R Akg 451/460 10 Conga 1 Shure sm 57/B57 Compr 11 Conga 2 Shure sm 57/B57 Compr 12 Timbales L Shure 81/Any condenser 13 Timbales R Shure 81/Any condenser 14 Bass amp D.I Compr 15 Bass mic Shure beta 57 Compr 16 Guitar Amp 1 Shure sm 57 17 Guitar Amp 2 Shure sm 57 18 Trombone Shure Beta 57 Compr 19 Trumpet Shure Beta 57 Compr 20 Saxophone Shure Beta 57 Compr 21 Vox 1 Shure Beta 58 Compr 22 Vox 2 Shure Beta 58 Compr 23 Vox 3 Shure Beta 58 Compr 24 Vox 4 Shure Beta 58 Compr 25 EFX 1 R 26 EFX 2 L 27 EFX 2 R 28 EFX 3 L 29 EFX 3 R 30 EFX 4 L 31 EFX 4 R 32 CD L 33 CD R FOH: 1. Mixing board must be: Midas, Soundcraft MH3 / MH4 , Yamaha , 32 channels min. 2. 12 channels of compression 3. 6 channels of gates 4. 2 channels of 1/3 octave EQ 5. 1 multi efx processor as Lexicon PCM 70/80/81 6. 2 multi efx processor as Yamaha SPX 90/990 7. 1 delay processor as Roland SDE 8. CD-Player Denon/Pioneer/Nad EXTRAS: Quicklock guitar stands

# Text boxes

CONGAS

BASS

M5

M4

##### DRUMSET

Guitar

2

Sax

MARKSCHEIDER KUNST

TECHNICAL RIDER

3 pages

Trumpet

Trombone

VOC 2

M36

M3

M1

M1

M2

M2

VOC 1

VOC 3

VOC 4

Guitar 1

Timbales

PERCUSSION